## Slide 1: Automated Image Quality Assessment in Medical Images
By: Faranak Dayyani & Sarina Taki

## Slide 2: Introduction:
Image Quality Assessment
  Important in image processing
  Helps with design decisions [1]
Three metrics:
  Noisy-ness (N) → amount of noise
    Common source: motion artifacts
  Contrast (C) → Resolution
  Edge Quality (E) → Fuzzy or sharp
Image quality represents the level of accuracy in imaging systems [1]
Dataset: Lung CT scans & Brain MRIs
[11]: https://openmedscience.com/radiology-radiography/

## Slide 3: Noisy-ness:
Definition: “Random variation of brightness or color information” [2]
Multiple methods
Chosen method: Peak signal-to-noise ratio (PSNR)
Unit : dB (decibel scale)
RMS equation [3][4]:
[12]: https://people.sc.fsu.edu/~jburkardt/c_src/image_denoise/image_denoise.html

## Slide 4: Contrast:
Well-known metric
Several methods [5]: similar results
  Weber
  Michelson
  RMS (Root-mean-square)
    Advantage:
      Simple
      Easy to understand
RMS: statistical measure
  Helps to identify patterns
  Equation [6]:
[13]: http://www.ianmorison.com/everything-about-refractors-ii-why-do-they-give-the-highest-contrast-images/

## Slide 5: Edge Quality:
Determine performance of edge detectors [7]
Various methods: MSE & SSIM [7]
  Both successful
  MSE → already used for measuring noisy-ness
  SSIM → too complex to implement
Method chosen: FM algorithm [8]
  Measures image sharpness
  7 steps
  Involves computing FT of input image
[14]: https://www.bogotobogo.com/python/OpenCV_Python/python_opencv3_Image_Canny_Edge_Detection.php

## Slide 6: Methods:
To measure image metrics by using three methods
PSNR measurement: noise-ness of the image [3].
RMS measurement: contrast of the image [10].
FM algorithm: Edge quality of the image [8].
[15]: https://doist.com/blog/personal-productivity-methods/

## Slide 7: Methods(Noise-ness):
PSNR method was used:
Convert the image type to double.
Filtered it by a Non-local mean filter.
Convert both input and filtered images to 8-bit signed integer.
Calculate MSE [3].
Calculate PSNR [3].
[16]:https://www.researchgate.net/figure/Illustration-of-the-PSNR-measure_fig6_268807675

## Slide 8: Methods(Contrast):
RMS method was used:
Convert the image type to double
Change the intensity range to [0 255] (Only for Lung CT)
Eliminate the zero pixels (Only for Lung CT)
Normalize the image
Calculate RMS [10].
[17]:https://uu.diva-portal.org/smash/get/diva2:1133556/FULLTEXT01.pdf

## Slide 9: Methods(Edge Quality):
FM algorithm was used [8]:
Convert the image type to double
Normalize the image
Compute frequency spectrum
Shift frequency spectrum to the center
Compute magnitude frequency
Compute maximum value of the magnitude frequency
Compute threshold
Compute number of pixels with intensity greater than the threshold
Compute image sharpness
[18]:https://www.sciencedirect.com/science/article/pii/S1877705813016007

## Slide 10: Results:
This table shows the values of PSNR, RMS and image sharpness for both Lung CT slice and Brain MRI volume images:

## Slide 11: Results(PSNR):
The image and histogram of a Lung CT slice with 0.5x noise for noise measurement
The image and histogram of a Brain MRI volume for noise measurement

## Slide 12: Results(RMS):
The image and histogram of a Lung CT slice with 0.5x noise for contrast measurement
The image and histogram of a Brain MRI volume for contrast measurement

## Slide 13: Results(FM algorithm):
The image and histogram of a Brain MRI volume for edge quality measurement
The image and histogram of a Lung CT slice with 0.5x noise for edge quality measurement

## Slide 14: Discussion:
Dataset: 1 slice of a lung CT scan, volume of a brain MRI
Lung CT slice:
  PSNR: 48.8718 → not noisy (in the 30 - 50 dB range)
  RMS: 0.4372 → low contrast, more dark regions (below 0.46291)
  FM: 0.0201 → strong edge quality ( > 0.014922)
Brain MRI volume:
  PSNR: 50.6745 → noisy (outside the 30 - 50 dB range)
  RMS: 0.5386 → high contrast (in the 0.46291 - 0.5537 range)
  FM: 0.0133 → weak edge quality ( < 0.014922)
Noisiness and edge quality are directly correlated
  Brain MRI is both noisy and has a weak edge quality, lung CT is the opposite

## Slide 15: Conclusion:
The purpose of this experiment is to measure the image quality based on three image quality metrics: image noisy-ness, contrast of the image and edge quality of the image.
PSNR was used to justify the noise quality of the image by computing the maximum signal to noise ratio [3].
RMS was used to justify the contrast quality of the image by identifying certain patterns in the image [5].
FM was used to justify the edge quality of the image by finding the total number of pixels with certain intensity in the non-shifted frequency spectrum of the image [8].

## Slide 16
The End.
Thank You
[19]:http://fallontrendpoint.blogspot.com/2006/05/who-really-owns-smiley.html

## Slide 17: References:
[1]BME 872 Biomedical Image Analysis, “Project: Automated Image Quality Assessment in Medical Images”, Ryerson University, Toronto, ON, rep., Winter 2020.
[2]A. Swain, “Noise in Digital Image Processing”, 24-Nov-2019. [Online]. Available: https://medium.com/image-vision/noise-in-digital-image-processing-55357c9fab71
[3]National Instruments, “Peak Signal-to-Noise Ratio as an Image Quality Metric”, 5-Mar-2019. [Online]. Available: https://www.ni.com/en-ca/innovations/white-papers/11/peak-signal-to-noise-ratio-as-an-image-quality-metric.html
[4]A. Robinson, “How to Calculate PSNR”, 2-Mar-2019. [Online]. Available: https://sciencing.com/how-to-calculate-psnr-12751768.html
[5]A. Shaus, S. F. Golovin, B. Sober, E. Turkel, & E. Piasetzky, (2017). “Potential Contrast – A New Image Quality Measure”, Image Quality and System Performance XIV, 14, 52–58, 2017. [Online]. Available: https://pdfs.semanticscholar.org/e3f2/e337d4470545398cc6753a54c21debf9c37b.pdf
[6]R. Gholipour-Peyvandi, S.Z. Islami-Rad, R. Heshmati, S. Zaferanlouie, & M. Ghannadi-Maragheh, “Influence of gamma emitter source intensity against energy on the image RMS contrast”. The Egyptian Journal of Radiology and Nuclear Medicine, 42(0378-603X), 425–431. 2011. doi: https://doi.org/10.1016/j.ejrnm.2011.10.003
[7]D. Sadykova, & A. P. James, “Quality Assessment Metrics for Edge Detection and Edge-aware Filtering: A Tutorial Review”, 1-Jan-2018. [Online]. Available: https://arxiv.org/pdf/1801.00454.pdf
[8]D. Kanjar, & V. Masilamani, “Image Sharpness Measure for Blurred Images in Frequency Domain”. Procedia Engineering, 64(18777058), 149–158. 2013. doi: 10.1016/j.proeng.2013.09.086
[9]S. Saladi, N. Amutha Prabha, “Analysis of denoising filters on MRI brain images”. Int. J. Imaging Syst. Technol. 27: 201– 208. 17-Aug-2017 https://doi-org.ezproxy.lib.ryerson.ca/10.1002/ima.22225
[10]D. G. Pelli, & P. Bex, “Measuring contrast sensitivity”. Vision Research, 90(0042-6989), 10–14. 213. doi: https://doi.org/10.1016/j.visres.2013.04.015